## Slide 1: Sinteza unitatilor de control microprogramate
- O compilatie eclectica pentru a avea un suport de discutie  -

## Slide 2
1940’s – Stored program computers
  Program instructions can be stored in memory along with data and can be manipulated like data
1947 – MIT Whirlwind: real-time flight simulator control store
  two-dimensional lattice
    rows – time sequence
    columns – control signals

## Slide 4
1951 – Maurice Wilkes
  Sequencing of control signals within the computer was similar to the sequencing actions required in a regular program.
  A stored program to represent the sequences of control signals. Called it microprogramming
  Divide machine instructions into subinstructions (microinstructions) that implement the instruction set of the machine
Full set of microinstructions made up the microprogram
1970’s
  Complex instruction sets
  Trend towards instruction sets very similar to high-level languages

## Slide 5
Control logic design
  Complex and error-prone
  Need a simpler method of developing the control logic for a computer
  Writing a program
    Simpler than designing the logic
    Easier to change
Benefits microprogramming offers
  More complex instructions can be implemented
  Less primitive than assembly
  Reduces field changes to defects

## Slide 6: Is Microprogramming Still Used Today?
ROM’s used to be faster than RAM, but not any longer
Control stores were implemented on ROM
Instruction sets have become much simpler (than the 1970s)
Less complexity
Computer-aided design tools have improved
  Yes, but benefits need to be weighed against costs:
  Complex ISAs such as IA-32 sometimes have more complex instructions implemented as microprograms.
  Pentium, Pentium 4, special-purpose processors, etc

## Slide 7: Control unit job is to generate the sequence of control signals How about building a computer to do this?
Develop microinstruction set
Write microprogram
Microassemble microprogram
Place the microassembled program (microcode) onto PLA or ROM

## Slide 8: Microcode “engine”
A computer to generate control signals is much simpler than an ordinary computer
At the simplest, it just reads the control signals in order from a read only memory
  The memory is called the control store
  Separate from program memory
  A control store word, or microinstruction, contains a bit pattern telling which control signals are true in a specific step
The major issue is sequencing
  In what order to read instructions?
  How will sequencing (next microinstruction to execute) be determined?

## Slide 9
Microinstruction has branch control, branch address, and control signal fields
Micro-program counter can be set from several sources to do the required sequencing
1. Next sequential
2. Start address of next macro inst.
3. Microinst specified address

## Slide 10: uP organization
Control signals are just read from memory, the main function is sequencing
This is reflected in the several ways the µPC can be loaded
  1. Output of incrementer—µPC+1
  2. PLA output—start address for a macroinstruction
  3. Branch address from µinstruction
  4. External source—say for exception or reset
Micro conditional branches can depend on condition codes, data path state, external signals, etc.

## Slide 12: Referinte suplimentare
http://people.cs.clemson.edu/~mark/uprog.html
http://www.cs.virginia.edu/~cs333/notes/microprogramming.pdf
http://research.microsoft.com/en-us/um/people/gbell/Computer_Structures__Readings_and_Examples/contents.html